## Slide 1: Session 3: Motion Planning for Manipulators
Jeremy Zoss
Sr. Research Engineer
Southwest Research Institute
5 June 2014

## Slide 2: Outline
Overview
  Motion Planning in ROS
HowTo: Set Up a New Robot
HowTo: Motion Planning using MoveIt!

## Slide 3: Motion Planning in ROS

## Slide 4: Motion Planning in ROS

## Slide 5: Traditional Robot Programming
Motion Types: limited, but well-defined. One motion task.
Environment Model: none
Execution Monitor: application-specific
J1
J2
P1
P2
Joint Move
J1
J2
Linear Move
P1
P2
User Application
Interpolate
Execute
Robot Controller

## Slide 6: ROS Motion Planning
Motion Types: flexible, goal-driven, with constraints
but minimal control over actual path
Environment Model: automatic, based on live sensor feedback
Execution Monitor: detects changes during motion
Move
Request
Start
Goal
User Application
Execute
Robot Controller
Planning
Filtering
ROS Motion Planning

## Slide 7: Motion Planning Components
Interactive
(rviz plugin)
ROS Actions
C++ API
Motion Planning
Collision Checking
Path Planning
Kinematics
Robot

## Slide 8: Motion-Control Components
Sensor Input
http://moveit.ros.org/wiki/index.php/Hydro/High-level_Overview_Diagram
http://moveit.ros.org/wiki/index.php/Hydro/Pipeline_Overview_Diagram

## Slide 9: Arm Nav. vs. MoveIt!
Arm Navigation
Released in 2011
  deprecated in Groovy
  stable, but obsoleted
Multiple nodes (8)
  extend by replacing nodes
Standard ROS Interfaces
  messages, services, actions, ...
Somewhat slow
  ROS comms. overhead
MoveIt!
Released in 2013
  API still evolving
One node
  component plugins
  extend by replacing plugins
Multi-Interfaces
  high-lvl API
  C++ objects
  messages, services, ...

## Slide 10: What Can MoveIt! Do?
http://www.youtube.com/embed/vAeEEoxVhAo?rel=0

## Slide 11: MoveIt! / Robot Integration
A MoveIt! Package...
  includes all required nodes, config, launch files
    motion planning, filtering, collision detection, etc.
  is unique to each individual robot model
    includes references to URDF robot data
  uses a standard interface to robots
    publish trajectory, listen to joint angles
  can (optionally) include workcell geometry
    e.g. for collision checking

## Slide 12: Exercise 3.1
Exercise 3.1:
Examining a Planning Environment

## Slide 13: HowTo: Set Up a New Robot

## Slide 14: Motivation
For each new robot model...
create a new MoveIt! package
Kinematics
  physical configuration, lengths, etc.
MoveIt! configuration
  plugins, default parameter values
  self-collision testing
  pre-defined poses
Robot connection
  FollowJointTrajectory Action name

## Slide 15: HowTo: Set Up a New Robot
Create a URDF
Create a MoveIt! Package
Update MoveIt! Package for ROS-I
Test on ROS-I Simulator
Test on “Real” Robot

## Slide 16: Create a URDF
Previously covered URDF basics.
Here are some tips:
  create from datasheet or use Solidworks Add-In
  double-check joint-offsets for accuracy
  round near-zero offsets (if appropriate)
  use “base_link” and “tool0”
  use simplified collision models
    convex-hull or primatives

## Slide 17: Verify the URDF
It is critical to verify that your URDF matches the physical robot:
  each joint moves as expected
  joint-coupling issues are identified
  min/max joint limits
  joint directions (pos/neg)
  correct zero-position, etc.

## Slide 18: Exercise 3.2
Exercise 3.2:
Verify the robot URDF

## Slide 19: Create a MoveIt! Package
Use the MoveIt! Setup Assistant
  can create a new package or edit an existing one

## Slide 20: Exercise 3.3
Exercise 3.3:
Create a MoveIt! Package
stop before tutorial step 2.1 (Test MoveIt Package). We’ll do that later.

## Slide 21: Update MoveIt! Package
Setup Assistant generates a generic package
  missing config. data to connect to a specific robot
  ROS-I robots use a standard interface

## Slide 22: Update MoveIt! Package
We’ll generate launch files to run both:
  simulated ROS-I robot
  real robot-controller interface
Joint_Names,
Points
- Point 1
- Point 2
...
FollowJointTrajectory Action
Joint Trajectory Action Server
ROS Industrial
MoveIt!
Arm Nav.
Custom Path
Industrial Robot Simulator
Motion Interface
State Interface

## Slide 23: Exercise 3.4
Exercise 3.4:
Update the MoveIt! Package for ROS-I
stop before tutorial step 3.1 (Test MoveIt Package). We’ll do that later.
SIA20D Joint Order:
S, L, E, U, R, B, T
SIA20D Substitutions:
[robot_moveit_config]
=> SIA20D_moveit_config
[robot_interface_pkg]
=> dx100

## Slide 24: HowTo: Motion Planning using MoveIt!
Motion Planning using RViz
Motion Planning using C++
Digging Deeper

## Slide 25: Motion Planning in RViz
Display Options

## Slide 26: Motion Planning in RViz
Planning Options

## Slide 27: Exercise 3.5
Exercise 3.5:
Motion Planning using RViz

## Slide 28: Motion Planning in C++
MoveIt! provides a high-level C++ API:
move_group_interface
#include <moveit/move_group_interface/move_group.h>
...
move_group_interface::MoveGroup group("manipulator");
group.setRandomTarget();
group.move();
3 lines = collision-aware path planning & execution
Amazing!

## Slide 29: Reminder: MoveIt! Complexity
Sensor Input
http://moveit.ros.org/wiki/index.php/Hydro/High-level_Overview_Diagram
http://moveit.ros.org/wiki/index.php/Hydro/Pipeline_Overview_Diagram

## Slide 30: Motion Planning in C++
Pre-defined position:
group.setNamedTarget(“home”);
group.move();
Joint position:
map<string, double> joints = my_function();
group.setJointValueTarget(joints);
group.move();
Cartesian position:
Affine3d pose = my_function();
group.setPoseTarget(joints);
group.move();

## Slide 31: Behind the Scenes
move()
move_group_interface
Start Pos,
Goal Pos,
Constraints,
...
MoveGroup Action
move_group
MoveIt!
Joint_Names,
Points
- Point 1
- Point 2
...
FollowJointTrajectory Action
Joint Trajectory Action Server
ROS-I

## Slide 32: Exercise 3.6
Exercise 3.6:
Motion Planning using C++

## Slide 33: Questions?
URDF
Setup Assistant
Robot Launch Files
RViz Planning
C++ Planning

## Slide 34: Contact Info.
Jeremy Zoss
Sr. Research Engineer
SwRI
9503 W. Commerce
San Antonio, TX 78227 USA
Phone: 210-522-3089 Email: jzoss@swri.org
www.ROSindustrial.org