## Slide 1: What Can You Do with ROS-I Today?
Shaun Edwards
Sr. Research Engineer
Southwest Research Institute
Slides Shamelessly Stolen from: Jeremy Zoss

## Slide 2: Overview
Hardware Support
  robots, sensors, interfaces
Capabilities
  simulation, planning, perception
Applications
  dynamic environments, smart control

## Slide 3: Hardware Support

## Slide 4: Industrial Robots
ABB
Fanuc
Adept
Motoman
Universal Robots

## Slide 5: New Robot Support
Easily add support for new robot models
  kinematics, STL meshes
  wizards: Solidworks, Arm Navigation
  config only. No software changes required!

## Slide 6: New Robot Support
Easily add support for new robot models
Framework for new robot controllers
  robot-side driver/server
  ROS client modifications (if needed)
  application code
  algorithms
  user-interface
  communications
  control
  feedback
  Robot Driver / Server
  motion commands
  status monitoring

## Slide 7: Imaging / Perception Sensors
2D Sensors
  cameras (ethernet, firewire)
  SICK laser rangefinder
3D Sensors
  stereo vision (bumblebee)
  kinect (structured light)
  swissranger (flash TOF)
And more!

## Slide 8: I/O Devices
Somewhat limited...
EtherCAT supported
  WAGO modules: DI/O, AI/O, etc.
  Robotiq gripper
Robot-connected I/O not supported (yet)

## Slide 9: Machine Tool Interface
ROS / MTConnect bridge
  communication and data-transfer
  synchronize robot tending with CNC operation
MTConnect / ROS
Bridge

## Slide 10: What’s Missing...
PLC Interfaces
Industrial Networks
  Ethernet/IP, DeviceNet, Modbus, Profibus, etc.
  OPC
Industrial HMIs

## Slide 11: Capabilities

## Slide 12: Perception
Segmentation
Identification
Mapping
Notes:   - identify discrete objects on a plane
  - filter out “known” objects (robot, environment)
  - monitor environment for changes
  - compare against DB to classify objects
- build a 2D map on-the-fly from sensor data
- track position in known map using sensor data

## Slide 13: Planning
Collision-aware path planning
  automatically finds path to target position
  avoids obstacles, joint limits, etc.
On-the-fly checks during execution

## Slide 14: Offline Development
Strong visualization environment
  review path-plans, debug control logic
  develop application even with no hardware
  enables smooth transition to physical system

## Slide 15: Offline Development
Strong visualization environment
Full physics-based simulation available
  includes simulated sensor feedback
Gazebo

## Slide 16: Offline Development
Strong visualization environment
Full physics-based simulation available
Can record and replay data
  both sensor and control data
  aids development and troubleshooting

## Slide 17: Online Visualization
Update visualization based on live sensor feedback
  remote process monitoring
  “augmented reality” displays

## Slide 18: Hardware Independence
Run the same program on different robot platforms.
  reduce software “porting” burden
  select robot based on capabilities, rather than familiarity

## Slide 19: What’s Missing
Precision control of path pos/vel/timing
Simplified programming interface
Motion-related triggers
  process control based on path timing
Dynamic path modification
  adjust motion based on sensor feedback

## Slide 20: Applications

## Slide 21: Unknown Part Stream
large, variable inventory
high-mix, low-lot production
Technologies
    3D scanning
    segmentation, filtering
    dynamic path planning

## Slide 22: Unstructured Picking
known parts, but random placement
partial occlusions
Technologies
    3D scanning
    segmentation
    filtering
    path planning

## Slide 23: Mobile Robots
inventory management
large workspaces
Technologies
    base / arm support
    mapping
    localization
    path planning
    navigation

## Slide 24: CAD &PLAN/SCAN & PLAN
Dynamic Painting, Deburring, Machining
Low Volume/High Mix
Technologies
    CAD/3D Scanning
    Semi-Constrained Path Planning
    Visualization

## Slide 25: Less-Industrial Applications
cook breakfast
fold laundry
play pool
bake cookies
fetch beer
scoop poop

## Slide 26: Summary
Hardware Support
  robots: fair, sensors: many, I/O: few
Capabilities
  3D perception and planning
Applications
  dynamic parts, environment, planning
  standard control/monitoring interfaces

## Slide 27: Contact Information
Shaun Edwards Senior Research Engineer
Southwest Research Institute
6220 Culebra Rd.
San Antonio, TX 78251 US
Phone: 210-522-3277 Email: sedwards@swri.org
www.rosindustrial.org
www.ros.org/wiki/Industrial