## Slide 1: Session 4: ROS-Industrial Introduction
Shaun Edwards
Sr. Research Engineer
Southwest Research Institute

## Slide 2: ROS-Industrial Overview

## Slide 3: Overview
Hardware Support
  robots, sensors, interfaces
Capabilities
  simulation, planning, perception
Applications
  dynamic environments, smart control

## Slide 4: Hardware Support

## Slide 5: Industrial Robots
Fanuc
ABB
Adept
Motoman
Universal Robots
Comau*
*Coming soon

## Slide 6: New Robot Support
Easily add support for new robot models
  kinematics, STL meshes
  wizards: Solidworks, Arm Navigation
  config only. No software changes required!

## Slide 7: New Robot Support
Easily add support for new robot models
Framework for new robot controllers
  robot-side driver/server
  ROS client modifications (if needed)
  application code
  algorithms
  user-interface
  communications
  control
  feedback
  Robot Driver / Server
  motion commands
  status monitoring

## Slide 8: Imaging / Perception Sensors
2D Sensors
  cameras (ethernet, firewire)
  SICK laser rangefinder
3D Sensors
  stereo vision (bumblebee)
  kinect (structured light)
  swissranger (flash TOF)
And more!

## Slide 9: I/O Devices
Somewhat limited...
EtherCAT supported
  WAGO modules: DI/O, AI/O, etc.
  Robotiq gripper
  Ronex
Robot-connected I/O – in progress
Many more: http://wiki.ros.org/Sensors

## Slide 10: Machine Tool Interface
ROS / MTConnect bridge
  communication and data-transfer
  synchronize robot tending with CNC operation
MTConnect / ROS
Bridge

## Slide 11: What’s Missing...
PLC Interfaces
  Integration of EPICS library planned (http://www.aps.anl.gov/epics/index.php )
Industrial Networks
  Ethernet/IP, DeviceNet, Modbus, Profibus, etc.
  OPC
Industrial HMIs

## Slide 12: Capabilities

## Slide 13: Perception
Segmentation
Identification
Mapping
Notes:   - identify discrete objects on a plane
  - filter out “known” objects (robot, environment)
  - monitor environment for changes
  - compare against DB to classify objects
- build a 2D map on-the-fly from sensor data
- track position in known map using sensor data

## Slide 14: Planning
Collision-aware path planning
  automatically finds path to target position
  avoids obstacles, joint limits, etc.
On-the-fly checks during execution

## Slide 15: Offline Development
Strong visualization environment
  review path-plans, debug control logic
  develop application even with no hardware
  enables smooth transition to physical system

## Slide 16: Offline Development
Strong visualization environment
Full physics-based simulation available
  includes simulated sensor feedback
Gazebo

## Slide 17: Offline Development
Strong visualization environment
Full physics-based simulation available
Can record and replay data
  both sensor and control data
  aids development and troubleshooting

## Slide 18: Online Visualization
Update visualization based on live sensor feedback
  remote process monitoring
  “augmented reality” displays

## Slide 19: Hardware Independence
Run the same program on different robot platforms.
  reduce software “porting” burden
  select robot based on capabilities, rather than familiarity

## Slide 20: What’s Missing
Precision control of path pos/vel/timing
Simplified programming interface
Motion-related triggers
  process control based on path timing
Dynamic path modification
  adjust motion based on sensor feedback

## Slide 21: Applications

## Slide 22: Unknown Part Stream
large, variable inventory
high-mix, low-lot production
Technologies
    3D scanning
    segmentation, filtering
    dynamic path planning

## Slide 23: Unstructured Picking
known parts, but random placement
partial occlusions
Technologies
    3D scanning
    segmentation
    filtering
    path planning

## Slide 24: Mobile Robots
inventory management
large workspaces
Technologies
    base / arm support
    mapping
    localization
    path planning
    navigation

## Slide 25: CAD &Plan/Scan & Plan
Dynamic Painting, Deburring, Machining
Low Volume/High Mix
Technologies
    CAD/3D Scanning
    Semi-Constrained Path Planning
    Visualization

## Slide 26: General Purpose Calibration
Current: Camera to Camera, Camera to Robot calibration
Future: Sensor to X, Robot kinematic calibration
Technologies
    2D/3D Processing
    Non-linear Optimization
    Visualization

## Slide 27: Less-Industrial Applications
cook breakfast
fold laundry
play pool
bake cookies
fetch beer
scoop poop

## Slide 28: Summary
Hardware Support
  robots: fair, sensors: many, I/O: few
Capabilities
  3D perception and planning
Applications
  dynamic parts, environment, planning
  standard control/monitoring interfaces

## Slide 29: Introduction to ROS-I (Users & Developers)

## Slide 30: Outline
Community
Wiki Documentation
Getting Help
Installing ROS

## Slide 31: Objectives
Learn how to participate and interact in the community
Understanding of ROS/ROS-I wiki
Know where and how to ask for help
Be able to install ROS-I from binary and source
Entertain you 

## Slide 32: ROS-I is a Community
Members: users, developers, researchers, bystanders, star trek fans(not star wars)
Resources:
  Wiki – http://ros.org/wiki/Industrial
  Email– http://groups.google.com/group/swri-ros-pkg-dev
  Forums – http://answers.ros.org/questions/
  Repos – http://github.com/organizations/ros-industrial

## Slide 33: ROS-I is a Community
Resources(cont):
  Twitter - https://twitter.com/ROSIndustrial
  Blog - http://rosindustrial.tumblr.com/
  YouTube channel - http://www.youtube.com/channel/UCXyGVRiCwUMc1gav-G7z2ew

## Slide 34: ROS-I is a Community
Community is managed, organized, and monitored by SwRI & RIC
  Monitored: Wiki, Group emails, Forums
  Access Controlled: Repos, Twitter, Blogs, YouTube channel

## Slide 35: ROS-I Wiki
A Wiki is a website which allows people to add, modify, or delete the content via a web browser usually using a simplified markup language or a rich-text editor. (http://en.wikipedia.org/wiki/Wiki)
It’s a Wiki, YOU can edit it!

## Slide 36: ROS-I Wiki
The ROS/ROS-I wiki contains documentation for users(focus) and developers
Documentation organized according to packages & stacks/meta-packages

## Slide 37: ROS-I Wiki
Users
  Overview
  Tutorials
Developers
Architecture/Design
Code API
Dependencies
Bug Tracker
  Typical Content

## Slide 38: Wiki Walkthroughs
ROS-I Wiki(follow): http://ros.org/wiki/Industrial
ROS-I Package Wiki (simple_message)(follow): http://ros.org/wiki/simple_message

## Slide 39: Getting Help
ROS Answers(follow): http://answers.ros.org/questions/
Developers List: http://groups.google.com/group/swri-ros-pkg-dev
  Join here: https://groups.google.com/group/swri-ros-pkg-dev/boxsubscribe

## Slide 40: Getting Help
Submitting Bugs (not for any code I have written)
  Github Code: http://github.com/organizations/ros-industrial/dashboard/issues
  Good bug submission:
    Setup, Steps to reproduce, Expected Results
  Best bug submission ever:
    Good submission + Test Code

## Slide 41: Getting Help
Call Us(Consortium Members Only)
  Paul Hvass W: 210-522-5823, Home: ….
Collaboration
  Generally open source
Consulting
  Whatever you want
  Various IP terms

## Slide 42: Installing ROS-I
Binary (using apt-get)
Recommended for users
Stable
Easy
Source (repos)
Required for developers
Github
Harder
Unstable*
Latest capability

## Slide 43: Binary Install
Command line: sudo apt-get install <package>
  ros-<version>-industrial-core
  ros-<version>-industrial-desktop
  ros-<version>-abb
  ros-<version>-motoman
  ros-<version>-fanuc
  ros-<version>-adept
  ros-<version>-universal-robotics

## Slide 44: Source Install
Wiki instructions(follow): http://ros.org/wiki/Industrial/Install
  Repository structure
  Experimental stacks/meta-packages

## Slide 45: Source Install (Git)
Install latest Groovy Industrial Core(example)
  Go to the wiki page for the industrial core stack/metapackage.
  Verify the required dependencies are installed on your system (exercise)
  Download the hydro version of the package to the current directory
  Build the stack

## Slide 46: Exercise
Exercise 4.1(follow) - https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.1

## Slide 47: ROS-I - Simple Message Layer (Core Developers)

## Slide 48: Outline
Overall Architecture
Simple Message Package Overview
Messages and Connections
Managers and Handlers
Library Linking

## Slide 49: Objectives
Understand the top-level ROS-I architecture
Be able to develop ROS-I simple message client/server applications
Understand how the simple message library can be used to bridge ROS messages to simple devices

## Slide 50: Top Level Architecture
Notes: Talk about different layers
Identify ROS-I App & Gui as future
Standard nodes are shown
Configuration data
Availability of ROS ecosystem, move it, and ros gui

## Slide 51: Simple Message Detail
Bridge layer between ROS and Robot Controllers

## Slide 52: Simple Message Package
Package Overview(follow): http://ros.org/wiki/simple_message
New Typed Messages (Post Groovy)
  Joint Trajectory Pt Full (mimics ROS JointTrajectoryPoint) http://ros.org/doc/api/trajectory_msgs/html/msg/JointTrajectoryPoint.html
  Robot Status (mimics ROS-I Robot Status) http://ros.org/doc/groovy/api/industrial_msgs/html/msg/RobotStatus.html
Notes: Motivation
Simple Message
Typed Messages
  joint
  joint traj pt full
  joint traj pt
  robot status
Simple Message Connections
  TCP Client/Servers
  UDP Client/Servers (experimental)

## Slide 53: Talker/Listener
Create 2 nodes, talker and listener
Send simple messages between nodes (NOT ROS messages)
Talker
Listener
Joint Simple
Message (request)
Joint Simple
Message (response)

## Slide 54: Create an Eclipse Project
Make eclipse project files
Import project into eclipse
Enjoy modern IDE features like code completion, syntax checking, etc…
Do not check project files into repos (they aren’t portable)

## Slide 55: Talker Node
// Initialize ROS node "sm_talker"
ros::init(argc, argv, "sm_talker");
// Required to start timers for non-node ROS use.
ros::Time::init();
// Little message to know she's started
ROS_INFO_STREAM("STARTING SM_TALKER");
// Create a TCP client connection to TCP_PORT on LOCAL_HOST (see common.h)
TcpClient client;
client.init(LOCAL_HOST, TCP_PORT);
while(!client.isConnected())
{
ROS_INFO_STREAM("Trying to connect to server");
client.makeConnect();
ros::Duration(0.5).sleep();
}
int seq = 0;
<continued>
while(client.isConnected())
{
// Create a message of type JointMessage and corresponding simple message
JointMessage jmReq;
SimpleMessage req, reply;
seq++;
jmReq.setSequence(seq);
jmReq.toRequest(req);
ROS_INFO_STREAM("Sending sequence number: " << seq);
client.sendAndReceiveMsg(req, reply);
ROS_INFO_STREAM("Received reply code: " << reply.getReplyCode());
ros::Duration(1.0).sleep();
}

## Slide 56: Listener Node
// Initialize ROS node "sm_talker" ros::init(argc, argv, "sm_listener"); // Required to start timers for non-node ROS use. ros::Time::init(); // Little message to know she's started ROS_INFO_STREAM("STARTING SM_LISTENER"); // Create a TCP server connection on TCP_PORT (see common.h) TcpServer server; server.init(TCP_PORT); while(!server.isConnected()) { ROS_INFO_STREAM("Trying to connect to client"); server.makeConnect(); ros::Duration(0.5).sleep(); } while(server.isConnected()) { // Create a message of type JointMessage JointMessage jmReq, jmReply; SimpleMessage req, reply; ROS_INFO_STREAM("Waiting for client request"); server.receiveMsg(req);
if( req.getMessageType() == jmReq.getMessageType() ) { if( req.getCommType() == CommTypes::SERVICE_REQUEST ) { jmReq.init(req); ROS_INFO_STREAM("Received sequence number: " << jmReq.getSequence()); jmReply.toReply(reply, ReplyTypes::SUCCESS); server.sendMsg(reply); ROS_INFO_STREAM("Sending reply code: " << reply.getReplyCode()); } else { ROS_ERROR_STREAM("Unexpected comm type: " << req.getCommType()); } } else { ROS_ERROR_STREAM("Unexpected message type: " << req.getMessageType()); } }

## Slide 57: Exercise
Exercise 4.2(Part 1) - https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.2

## Slide 58: Message Manager/Handler
Message manager/handlers simplify relaying simple messages (similar to ROS msg callbacks)
Allows multiple data streams to use the same connection

## Slide 59: Library Linking
Simple Message compiled as a library for inclusion in other packages
  2 versions compiled (normal, byte swapped)
Linking to Simple Message library (non-standard)
  Example: http://ros.org/wiki/simple_message#Library_Linking

## Slide 60: Message Handler
// Handler class defined specifically for this example class MyHandler : public MessageHandler { // since this class defines a different init(), this helps find the base-class init() using MessageHandler::init; public: bool init(SmplMsgConnection* connection) { return this->init(StandardMsgTypes::JOINT, connection); } private: bool internalCB(industrial::simple_message::SimpleMessage & in) { bool rtn = false; JointMessage jm; SimpleMessage msg; if (jm.init(in)) { ROS_INFO_STREAM("Received sequence number: " << jm.getSequence());
if (jm.toReply(msg, ReplyTypes::SUCCESS)) { if (this->getConnection()->sendMsg(msg)) { ROS_INFO_STREAM("Sending reply code: " << msg.getReplyCode()); rtn = true; } else { ROS_ERROR("Failed to send joint message return"); rtn = false; } } else { ROS_ERROR("Failed to generate joint reply message"); rtn = false; } } else { ROS_ERROR("Failed to initialize joint message"); rtn = false; } return rtn; } };

## Slide 61: Manager
// Initialize ROS node "sm_talker" ros::init(argc, argv, "sm_listener"); // Required to start timers for non-node ROS use. ros::Time::init(); // Little message to know she's started ROS_INFO_STREAM("STARTING SM_MANAGER");
TcpServer server; server.init(TCP_PORT); MessageManager manager; MyHandler handler; manager.init(&server); handler.init(&server); manager.add(&handler); manager.spin();

## Slide 62: Exercise
Exercise 4.2(Part 2) - https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.2

## Slide 63: ROS-I - Interface Layer (Core Developers)

## Slide 64: Outline
Industrial Robot Driver Specification
Industrial Messages
Industrial Robot Clients
Industrial Robot Simulator
Joint Trajectory Filters

## Slide 65: Objectives
Understand the motivation and function of the ROS-Industrial Driver Specification
Understand how to use of the industrial robot clients as standard nodes for talking to robot controllers
Understand how to use the industrial robot simulator
Awareness of the joint trajectory filter package

## Slide 66: Simple Detail
Bridge layer between simple message and high level software

## Slide 67: ROS-Industrial Specification
ROS-I Wiki(follow): http://ros.org/wiki/Industrial/Industrial_Robot_Driver_Spec
Notes: Motivation
Minimal
Full
Hardware Compatibility
Future

## Slide 68: Industrial Messages
ROS-I Wiki(follow): http://ros.org/wiki/industrial_msgs
Notes: Robot status
Motion command service
JointTrajectory
JointStates

## Slide 69: Industrial Robot Clients
ROS-I Wiki: http://ros.org/wiki/industrial_robot_client
3 Types of nodes
  Motion (command joint motion)
    Streaming & download
  State (joint positions and status)
  Joint Trajectory Action (Follow joint trajectory action server)
Motion
Node
State
Node
Action
Node
Notes: Client nodes adhere to the ROS-I spec

## Slide 70: Industrial Robot Simulator
Different from MoveIt Simulator
ROS-I Wiki: http://ros.org/wiki/industrial_robot_simulator
Simulates both robot motion and state nodes (i.e. adheres to spec)
Allows quick development without hardware
Action
Node
Sim
Node

## Slide 71: Joint Trajectory Filters
Experimental (Post Groovy)
Every moveit/arm navigation package has a joint_limits.yaml. See: http://ros.org/wiki/trajectory_filters
ROS-I Wiki (follow): http://ros.org/wiki/industrial_trajectory_filters
Very useful for smoothing out and improving joint motion.

## Slide 72: Introduction to Using ROS-I (app Developers)

## Slide 73: Outline
Top Level Architecture
Application Layer
GUI Layer
Common Application Tasks

## Slide 74: Objectives
Understand the various ways to create application level programs
Understand the interface layer(s)
Understand the possibilities
Steps to build up to an application

## Slide 75: Top Level Architecture
Notes: Application layer
Joint Trajectory action interface/ROS-I spec interface

## Slide 76: Application Layer
ROS Layer
  Anything you can imagine
MoveIt Layer
  Planning
  Kinematics
  Pick & Place
  Workspace evaluation
ROS-I Layer (Future)
  Process based planner
  Industrial state machines

## Slide 77: GUI Layer
ROS GUI
  Qt based GUI
    Powerful
    Widget based
    Cross platform (although ROS isn’t)
ROS-I GUI (Future)
  Generic pendant
  Standard industrial UI
  Industrial Widgets

## Slide 78: Applications Building
Create MoveIt configuration for your application
Verify configuration with physical robot cell (exercise 4.3)
Tweak motion to meet your needs (exercise 4.4)
Build your application code (application specific)
Build GUI interface (application specific)

## Slide 79: Machine Tending Application
Robot, CNC, & Caging
Verify robot and physical layout
Fast motion for large moves, fine motion for interfacing with external equipment
Create industry standard state machine (start, stop, fault reset interface)
Create GUI that has buttons for changing modes, error logs, visualization.

## Slide 80: Robot Package Verification
Exercise 4.3 https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.3

## Slide 81: Improving Robot Motion
Exercise 4.4 https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.4

## Slide 82: Future ROS-I Development

## Slide 83: Outline
What the Future Holds
Please Share Your Ideas

## Slide 84: Objectives
Tell you where we are going
Ask you where you want us to go

## Slide 85: What's next?
Flexible robot IO control
Improved drivers (vendor supported)
Improved calibration support (single pass robot cell calibration)
Generalized process aware Cartesian path planners

## Slide 86: Standard GUI

## Slide 87: Code Metrics/Unit Tests
Jenkins continuous integration

## Slide 88: Robot Task Description Format
XML file format for describing arbitrary motion
Expressive enough for high/low density waypoints
Encapsulates process data

## Slide 89: Roadmap
ROS-I Wiki (follow): http://ros.org/wiki/Industrial/Roadmap

## Slide 90: What do YOU want?

## Slide 91: Introduction to Perception

## Slide 92: Outline
Explanation of the Perception Tools Available in ROS
Kinect Introduction

## Slide 93: Objectives
Cursory understanding of the perception tools
Experience with Kinect data and tools

## Slide 94: Example: Pick & Place

## Slide 95: Perception Libraries
Point Cloud Library (PCL) - http://pointclouds.org/
  Focused on 3D Range(Colorized) data
http://pointclouds.org

## Slide 96: Perception Libraries
Open Computer Vision Library (OpenCv) - http://opencv.org/
  Focused on 2D images
  2D Image processing
  Video
  Sensor calibration
  2D features
  GUI
  GPU acceleration
http://opencv.org

## Slide 97: ROS Bridges
OpenCV & PCL are external libraries
“Bridges” are created to adapt the libraries to the ROS architecture
  OpenCV: http://ros.org/wiki/vision_opencv
  PCL: http://ros.org/wiki/pcl_ros
    Standard Nodes: http://ros.org/wiki/pcl_ros#ROS_nodelets

## Slide 98: Many More Libraries
Many more libraries in the ROS Ecosystem
  AR Tracker - http://www.ros.org/wiki/ar_track_alvar
  Object Recognition - http://www.ros.org/wiki/object_recognition
  Robot Self Filter - http://www.ros.org/wiki/robot_self_filter
  Let me Google that for you  - http://bit.ly/12PebaA

## Slide 99: Exercise
Exercise 4.5 - https://aeswiki.datasys.swri.edu/rositraining/Exercises/4.5

## Slide 100: Contact Information
Shaun Edwards Senior Research Engineer
Southwest Research Institute
6220 Culebra Rd.
San Antonio, TX 78251 US
Phone: 210-522-3277 Email: sedwards@swri.org
www.rosindustrial.org
www.ros.org/wiki/Industrial